## Slide 1: A Survey of Finishing Wood
Common Stains, Finishers, and Sealers
By Cody Hanson for the Olympia Woodworkers Guild December 2023

## Slide 2: Pantheon of Finishing
  Natural – Anything grown in nature, refined for use Synthetic – Anything derived from a lab Stains – Things that change your mediums’ color Finishers – Things that protect the surface, but don’t seal pores Sealers – Things that protect the surface/seal pores Mixers – Things that thin one item or mix multiple items

## Slide 3: Naturals: Stains/Finishers/Sealers

## Slide 4: Linseed Oil
Linum Usitatissimum
Previously called Linum or Linus, now called Flax

## Slide 5: Linseed Oil
Linseed cultivation confirmed as early as 9000 years ago (7000 BC)
First documented in Ancient Sumeria 5900 BC
Used as an additive to cereals, for sealing wood, and oiling metals.

## Slide 6: Linseed Oil
Key ingredient in paints, putty's, glazes, wood sealers, animal feed, leather treatment, iron/steel treatment, etc
Active mass production from 5900 BC – 1950s AD, nearly 8000 years. Is a “drying” oil. Is often absorbed by substance and hardens when dried.
Adds a slight yellow taint to wood and can take weeks to feel dry to the touch. Won’t fully cure for months (if you can smell it, it’s not cured)
Notes: Sumeria wood
Egyptian Paints
Roman Oils
1861 – 1m gallons/year, 1870 – 12m. 1890 – 48m, 1920 – 335m, 1940 – 810m, 1975 – 810m
Additives. Blacking, lead oxide/white lead – tetra ethyl lead
Brush, wipe, spray

## Slide 7
First attested use was in 2650 BC for writing
Candle use first attested 2600 BC
First documented case of Beeswax on wood, 200 BC
Beeswax

## Slide 8: Danish Oil
Mix of Linseed Oil and Beeswax
Gets its name from “Danish” workers hired to do wood and stone work in 7th century Europe, who readily used the mix
Name was revived in the 1950s by Swedish Furniture manufacturers as a marketing name for the distinctive “old world” look.
Traditionally 1 part wax to 3 parts oil
Modern mixes

## Slide 9: Carnauba Wax
Copernicia Prunifera, Carnauba Palm
Native to Brazil. First used commercially as a wax in the late 1700s
Frequently mixed into beeswax from 1800s on to create a smoother application
Notes: Glossy vs beeswax matte
Higher melting point
white/ vs yellow
Harder to apply, but longer lasting Mixed in with a lot

## Slide 10: Tung Oil
Vernicia fordii, Tung Tree
First documented 500 BC
Primarily used to seal ships
  was discovered by western nations in 1642
  Often mixed with Linseed Oil
  Still used for boats and outdoor furniture
Modern mixes
Notes: Modern polyurethane mixes
Brush, don’t wipe.
Can thin

## Slide 11: Shellac
Literally She – Lac. Wax substance produced by the female Lac beetle as it eats the Kusum tree (Schleichera oleosa)
Dissolves in alcohol
Most recently application merges with each previous application

## Slide 12: Shellac: Fine Furniture
French Polish: Linen + ground pumice + shellac
Two Methods:
  French – soak the linen + pumice in shellac, apply. Repeat 8-10 times
  English – apply shellac, then sand with linen + pumice. Repeat 8-10 times

## Slide 13: Lacquer: Eastern
Distilled sap of the Toxicodendron vernicifluum, the Lacquer tree
  Present in Japan 12,000 years ago
Multiple types
  Unrefined is 25% water, Brown
  In its refined state is clear
    Japanese name changes based on the dye added to it
    Linseed oil sometimes added for sheen
  NOT JAPPANING

## Slide 14: Lacquer: Western
Is a Shellac based product (thus the name)
First appears in the 1600s
Resins dissolved in alcohol create color bases
Mix into shellac, add pine resin, add turpentine
Shake

## Slide 15: Varnish
From the Latin – Vernix, meaning “foul smelling resin’’
1 Part drying oil + 1 part resin + 1 part solvent
Most common recipe, Linseed oil, Pine Sap, Turpentine
In use from Ancient times to 1950s
Boats, clothing, floors

## Slide 16: Naturals: Stains

## Slide 17: Ammonia Hydroxide
Used for “Fuming”, not application
Reacts to Tannins in wood
Notes: Quertannic acid – Tannin
Oak, maple, spruce, larch, mahogany,chestnut, elm,
% varies.

## Slide 18: Sodium Hydroxide
Lye
Reacts to Tannins
Ages wood

## Slide 19: Iron Acetate
Buff Iron
Reacts to Tannins
Rusted Iron in water, mixed to a 50:50 solution with vinegar
Turns Solid black

## Slide 20: Sodium Borate
Borax
Prevents Mold
Prevents boring insects

## Slide 21: Potassium Dichromate
Extremely Toxic to touch and smell.
Used originally for “Tanning”, leathers, wood, printing, and film.
Ceramics Glazing

## Slide 22: Naturals: Solvents

## Slide 23: Turpentine
From the Greek Terebinthine - “resin”
Orginally used the Terebinth tree, but moved to Pine.
  In the US, Eastern White Pine then Western White Pine
Used in EVERYTHING
Notes: Toxic
Bio Solvent
Pine sap, distilled into liquid.

## Slide 24: Synthetics: Solvents

## Slide 25: False Turpentine
Oil Solvent
Chemically complicated or 1 step from Diesel
Became known as White Spirits, Petroleum Spirits, or Mineral Spirits

## Slide 26: Synthetics: Dyes

## Slide 27: Aniline
William Henry Perkin
At age 18, 1856 made his discovery while looking for a synthetic cure to Malaria.
Notes: Mauvine

## Slide 28: Aniline Wood Dyes
Generally refers to dried powder dyes requiring Oil, Water, or Alcohol to become usable
Notes: Lee Valley Dyes
W. D. Lockwood Dyes (Tools for woodworking)
J.E. Moser's
Trans Tint

## Slide 29: Oil Stains/Paints
Traditional Way of staining
Aniline Dye + Linseed Oil Usually includes dyer agents
Really only works on hardwoods
Prefers planned surfaces vs sanded
High VOC, requires near instant cleanup Mineral Spirits
Doesn’t raise the grain

## Slide 30: Water Stains
Modern way to stain
Aniline Dye + Water + Evaporating agent
Works on most woods
Low VOC, Easy clean up, wash with water
Prefers sanded surfaces vs planed ones
Raises the grain

## Slide 31: Gel Stains
Invented 1960s
Aniline Dye + Linseed Oil + synthetic jelly + Urethane
Works on all woods, already finished surfaces, non-wood surfaces
Doesn’t raise the grain
Doesn’t blotch, can stain finished woods
Higher VOC than Water based, lower than traditional oil based.
Requires Mineral Spirits for cleaning

## Slide 32: Synthetics: Finishers/Sealers

## Slide 33: Mineral Oil
Liquid Paraffin or White Oil
Simply liquid Petroleum Jelly

## Slide 34: Polyurethane
Discovered 1937 by Otto Bayer, was interrupted and resumed production in 1952
Isocyanate with a Polyol
45k metric tons 1960 -> 25 million metric tons produced annually 2020
Notes: By 1957 Poly accounted for 55% of wood finishing market

## Slide 35: Urethane
Polyisocyanate + Polyol then stripping of the double Poly bond leaving a thin, strong, clear liquid

## Slide 36: Marine Variants
Urethane with UV protection additives PLUS :
  Water Based + evaporators
  Linseed Oil Based with dryers
  Tung Oil

## Slide 37
Thanks!
Comments/Questions?